## Slide 1
CONTINUING PROFESSIONAL DEVELOPMENT
Polychem Systems
Purex NG OC500 & CC2000
Spray Foam Insulation
Presented by Adrian Sheils
SprayFoam Direct Distribution – Official Irish Distributor
15-minute CPD • Open-cell OC500 • Closed-cell CC2000 • Irish U-value context
sprayfoamdirect.ie | Roscrea Rd, Crinkill, Co. Offaly

## Slide 2
About Your Presenter
Adrian Sheils
Founder & Director
SprayFoam Direct Distribution
Official Irish Distributor for
Polychem Systems
Nationwide supply and technical
support for Purex NG OC500
and Purex CC2000
Distribution focus
Supplying Purex NG OC500 (open-cell) and Purex CC2000 (closed-cell) across Ireland
Technical support
Product selection, application advice and training support for installers
Local knowledge
Deep understanding of Irish building types, climate and regulatory requirements
Contact
087 632 3186 • +353 57 910 6004
info@sprayfoamdirectdistribution.ie
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
2 / 12

## Slide 3
Agenda
01
What is spray polyurethane foam (SPF)?
02
Open-cell vs closed-cell – key differences
03
Purex NG OC500 (open-cell) & Purex CC2000 (closed-cell)
04
Performance data & U-value context
05
Where to specify each product
06
Irish context: NSAI, Building Regulations & SEAI
07
Installation quality & key takeaways
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
3 / 12

## Slide 4
What is Spray Polyurethane Foam?
Two-component system (isocyanate + polyol) mixed at the gun and sprayed under high pressure. Expands in place to form a continuous, seamless insulation layer that also acts as an air barrier.
Thermal Insulation
Low thermal conductivity. Fills irregular cavities completely and helps achieve target U-values without thermal bridges.
Air Barrier
Continuous seal reduces uncontrolled air leakage – a major source of heat loss in Irish dwellings.
Versatile Application
Attics, walls, floors, roofs, industrial & agricultural buildings. Adheres to timber, masonry, metal, concrete.
4 / 12
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems

## Slide 5
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
3 / 12

## Slide 6
Open-Cell vs Closed-Cell
OPEN-CELL – Purex NG OC500
▸ Density: typically 8–12 kg/m³
▸ λ ≈ 0.036–0.038 W/m·K
▸ Soft, flexible, vapour-permeable
▸ Excellent acoustic absorption
▸ Expands ~100× liquid volume
▸ Best for interiors: attics, walls, ceilings
▸ Lower installed cost per m2
▸ Not for continuous water exposure
CLOSED-CELL – Purex CC2000
▸ Density: typically 30–40 kg/m³
▸ λ ≈ 0.022–0.025 W/m·K
▸ Rigid, high compressive strength
▸ Very low water absorption
▸ Acts as vapour retarder
▸ Suitable for exterior & below-grade
▸ Higher performance per mm of thickness
▸ Adds structural racking strength
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
5 / 12

## Slide 7
The Two Products We Supply
Purex NG OC500
Open-cell spray foam
• Low-density open-cell structure
• Thermal & acoustic insulation
• Internal applications – attics, walls, ceilings
• Vapour-permeable
• Excellent air sealing when applied correctly
• CE marked to EN 14315-1
Purex CC2000
Closed-cell spray foam
• Medium-density closed-cell structure
• High thermal performance per mm
• Internal & external applications
• Very low water absorption
• Vapour retarder + structural contribution
• CE marked to EN 14315-1
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
6 / 12

## Slide 8
Performance & U-Value Context
In Ireland we design and specify using U-values (W/m²K). The lower the U-value, the better the thermal performance of the building element.
Property | Purex NG OC500 | Purex CC2000
Type | Open-cell | Closed-cell
Typical density | 8–12 kg/m³ | 30–40 kg/m³
λ (W/m·K) | ≈ 0.036–0.038 | ≈ 0.022–0.025
Structure | Soft / flexible | Rigid
Vapour behaviour | Vapour-permeable | Vapour retarder
Water absorption | Higher | Very low
Primary use | Internal attics & walls | Agri and commercial
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
7 / 12

## Slide 9
Where to Specify Each Product
Prefer Purex NG OC500
• Attics & loft conversions (internal)
• Internal walls & partitions
• Ceilings & suspended floors
• Where acoustic performance matters
• Projects prioritising vapour openness
• Budget-sensitive large-volume fills
Prefer Purex CC2000
• Flat roofs & external roof decks
• Foundations & below-grade walls
• Industrial / agricultural buildings
• Cold stores & high-moisture areas
• Where high compressive strength needed
• Limited cavity depth (better U-value per mm)
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
8 / 12

## Slide 10
Irish Regulatory Context
NSAI Certification
For SEAI grant eligibility and proven suitability under Irish site conditions, the specific foam system should hold a current NSAI Certificate confirming compliance with Building Regulations.
Building Regulations
Part L (Conservation of Fuel & Energy) sets elemental U-value targets. Part F (Ventilation) is critical when airtightness is improved. Part B (Fire) covers reaction-to-fire and thermal/ignition barriers.
SEAI Grants
Attic insulation and other measures remain grant-aided when installed by registered contractors using products that meet the scheme’s technical requirements (typically NSAI Certification & correct detailing).
Best Practice
Follow the NSAI Certificate scope: AVCL where required, residual ventilation, thickness limits per pass, and installer competence. Incorrect detailing is the main source of reported issues.
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
9 / 12

## Slide 11
Key Performance Benefits
01
Seamless air seal
Eliminates gaps and thermal bridging common with batts or boards – supports better U-values
02
Target U-values
Closed-cell CC2000 delivers strong thermal performance in limited depth
03
Moisture control options
CC2000 resists water; OC500 allows greater drying potential
04
Acoustic performance
OC500 open-cell systems provide excellent sound absorption
05
Structural contribution
CC2000 can increase racking strength of framed assemblies
06
Long-term stability
Declared parameter stability when correctly installed and detailed
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
10 / 12

## Slide 12
Installation & Quality Essentials
Trained applicators only
High-pressure equipment, correct temperatures, ratio control and PPE are mandatory. Quality depends heavily on installer skill.
Layer thickness & curing
Respect maximum pass thickness and inter-pass times. Over-application can cause shrinkage or incomplete curing.
Substrate preparation
Clean, dry, suitable temperature. Excellent adhesion is a strength – but only on properly prepared surfaces.
Fire & thermal barriers
Where required by Building Regulations, install approved thermal/ignition barriers (e.g. plasterboard) over the foam.
Ventilation & AVCL
Follow the product’s Certification or technical guidance for vapour control layers and residual ventilation needs.
Documentation
Record product batch, thickness achieved, installer details and any Certificate of Compliance for BER / handover.
Adrian Sheils | SprayFoam Direct Distribution | Official Irish Distributor – Polychem Systems
11 / 12

## Slide 13
Key Takeaways
1.
Purex NG OC500 (open-cell): lower density, vapour-open, strong acoustic performance – ideal for internal attics and walls.
2.
Purex CC2000 (closed-cell): higher performance per mm, moisture resistance, structural contribution – preferred for Agri,commercial and demanding environments.
3.
Both systems are CE-marked and supplied in Ireland by SprayFoam Direct Distribution.
4.
Specify systems that carry NSAI Certification where grant funding or formal compliance evidence is required. Design to target U-values.
5.
Correct installation and detailing determine long-term performance far more than the product alone.
Questions? Contact Adrian Sheils • 087 632 3186 • info@sprayfoamdirectdistribution.ie
SprayFoam Direct Distribution | Roscrea Rd, Crinkill, Co. Offaly | Official Irish Distributor – Polychem Systems
www.sprayfoams.ie